SSUSI PREP Data File Definition

APL Data Product Version = 0105

Change Log

| Revision | Date | Change |
| --- | --- | --- |
| 1.5.0 | 3/28/08 | Added FirstYear, LastYear NetCDF fields |
| 1.4.0 | 2/8/2007 | Scan_type changed to Scan_mode |
| 1.3.0 | 1/11/2007 | Added Scan_Type field to easily discriminate between Full and Reduced Scans |
| 1.2.0 | 7/19/2006 | Added data product version number to document. |
| 1.1 | 4/19/2006 | Added nodal second |
| 1.0 | 4/12/2006 | Initial version taken from SSUSI data formats document |

SSUSI PREP Data File Definition	1

1	Introduction	2

2	Data Product Filename	2

3	Prep File	2

3.1	Format of Readout Information Record in Prep File.	3

3.2	Format of GWC Ephemeris Record in Prep File	4

3.3	Format of Z-Bits Ephemeris Record in Prep File.	5

3.4	SSUSI Sensor Data Record.	6

3.5	Sensor Data Packet Record.	7

3.6	Sensor Data Packet Header	7

3.7	Packet Data formats by Packet ID	8

3.7.1	Fill Packets	8

3.7.2	Full Image Scan	8

3.7.3	Reduced Scan Packets	11

3.7.4	Spectrograph mode	14

3.7.5	Maintenance Mode	16

3.7.6	Setup Mode	18

3.7.7	Test Mode	20

3.8	Supporting Data Prep File.	22

# Introduction

This document describes the detailed formats of the data products that will be made by the UNIX based IDL and C++ processing system for the SSUSI instrument on DMSP spacecraft.  This table is based on information from the old ADA based Software Design Document, but reflects changes made to the processing system.

We begin with a description of the Data Product file naming convention and then describe the data in order of processing, beginning with PREP files (which are reformatted raw data from the Raw Sensor Data Records received from the air force.).  It then moves on to describe Level 1B, SDR, and various EDR data products.

# Data Product Filename

- SSUSIFpp_Svaaaarbbb_yyyydoyREVoooooQOzz.mode_filetype:  for all Prep files that encompass a single quarter orbit with a single scan overlap into adjoining quarter orbits

- where

- pp is the DMSP satellite number, with valid ranges of F01 through F20

- mode is the instrument mode.  Allowable modes are as follows and are case sensitive:

- image - for imaging mode

- spect - for spectrograph mode

- maint – for maintenance mode

- test – for test mode

- S is the facility that generated the SSUSI data product.  Allowable facilities are as follows and are case sensitive:

- A – for JHU/APL

- S – for Aerospace

- F – for AFWA

- aaaa is the 4 digit data product version number (this number combined with the revision number makes the data product file unique).  "v" always precedes this indicating that this is a version number.

- bbb is the 3 digit data product revision number (this number combined with the version number makes the data product file unique).  "r" always precedes this indicating that this is a revision number.

- yyyy is the 4 digit year.  For multiple orbits, the first is start and the second is stop

- doy is the 3 digit day of the year.

- ooooo is the orbit number.  For multiple orbits, the first is start and the second is stop

- zz is the quarter orbit designator number.  Allowable choices are as follows and are case sensitive:

- NP – for North Polar

- SP – for Southern Polar

- DE – for Descending Equatorial

- AE – for Ascending Equatorial

- Filetype is the type of data product type in this case the type is PREP.

# Prep File

This is an internal file produced by the BNSA software and its intent is to be ingested by the SSUSI Engineering POC and the APSB software.  The data in this file contains compressed pixel data.  It is unprocessed instrument data at full resolution, time-tagged, s/c location specified and tagged with a preliminary data quality flag.  These files are constructed from DMSP “raw” files also called Raw Sensor Data Records (RSDRs) by the Data Reformatter in order to construct SSUSI Data product Files. The data is time ordered but stored in reverse chronological order which is how the RSDRs are received.

- per file

| Data Item | Data Type | Field Size (Bytes) | Range or Nominal Value | Units |
| --- | --- | --- | --- | --- |
| Header | N/A | 1637 | N/A | N/A |

## Format of Readout Information Record in Prep File.

There is only one Readout Information Record per Prep File.

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content Notes |
| --- | --- | --- | --- | --- | --- |
| -Mission ID | Mission | string | 4 |  | 4 characters, e.g. “F16” |
| -Readout Rev | ReadoutRev | Integer | 4 | 1.. 4,294,967,295 | Satellite revolution number |
| -Nodal Long | NodalLong | integer | 4 | 0..3600 | East from Greenwich meridian for ascending nodal crossing of readout rev |
| -Nodal Julhr | NodalJulHr | integer | 4 | 0..34359738367 | AFGWC system time of readout rev nodal crossing relative to 0000Z on 12/31/67 |
| -Nodal Day | NodalDay | integer | 4 | 1..31 | “ |
| -Nodal Month | NodalMonth | integer | 4 | 1..12 | “ |
| -Nodal Year | NodalYear | integer | 4 | 0..99 | “ |
| -Nodal Time | NodalTime | integer | 4 | 0..2359 | 100x hour of day + minute of hour |
| *Nodal Second | NodalSecond | Integer | 2 | 0..59 | Seconds of the day |
| -Orbital Inclination | OrbitalInclination |  | 2 | TBD | Angle between the orbital plane and the equatorial plane. Range of 0 to pi. Stored as radians * TBD. |
| -Right Ascension of the Ascending Node | RAAN |  | 4 | TBD | Angle, measured at the center of the earth, from the vernal equinox to the ascending node. Range of 0 to 2 * pi. Stored as radians *TBD. |
| *RSDR Specification Version Number | RSDRSpec | integer | 2 | 8..6553 | Represents the version number taken from the DMSP Satellite RSDR File Format Specification. Stored as version number * 10 to allow for incrementing a version number by tenths. |
| -Minute Count (array of 2 or array of 8 bytes) | MinuteCount | byte | 8 No 8 byte integers | 1..34359738367 | minutes of data in this readout |
| -First Year | FirstYear | Integer | 4 | 2003-2100 | Year for latest record in Prep file |
| -First Julday | FirstJulDay | integer | 4 | 1..366 | Day of year for latest record in Prep file |
| -First Hour | FirstHour | integer | 4 | 0..23 | Hour of day for latest record in Prep file |
| -First Minute | FirstMinute | integer | 4 | 0..59 | Minute of hour for latest record in Prep file |
| -First Second | FirstSecond | integer | 4 | 0..59 | Second of minute for latest record in Prep file |
| -Last Year | LastYear | Integer | 4 | 2003-2100 | Year for latest record in Prep file |
| -Last Julday | LastJulDay | integer | 4 | 1..366 | Day of year for earliest record in Prep file |
| -Last Hour | LastHour | integer | 4 | 0..23 | Hour of day for earliest record in Prep file |
| -Last Minute | LastMinute | integer | 4 | 0..59 | Minute of hour for earliest record in Prep file |
| -Last Second | LastSecond | integer | 4 | 0..59 | Second of minute for earliest record in Prep file |
| -RSDR File Name | RSDRFilename | String | 60 |  | The name of the source RSDR file |
| -Prepfile Name | Filename | String | 60 |  | The name of this file |
| -R+ Number | R+Number | integer | 4 | 0 .. 14 | Readout rev number relative to beginning of satellite day (beginning at or west of 68.1W) |
| Total size |  |  | 130 |  |  |

## Format of GWC Ephemeris Record in Prep File

There is one ephemeris record for all of the SSUSI sensor data records in a given scan.    Therefore, for imaging mode, there is 22 seconds in a scan so there will be one ephemeris record associated with all 22 seconds of the SSUSI sensor data.  For spectrograph mode, there is 3 seconds in a scan so there will be one ephemeris record associated with all 3 seconds of the SSUSI sensor data.   For test, maintenance and setup modes, there is 1 second in a scan so there will be one ephemeris record associated with each 1 second of the SSUSI sensor data.

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| -Lat.,_1, Long._1 | Lat_1, Long_1, | Float | 2 x 4 | Float32 |  |
| -Altitude_1 | Alt_1 | Integer | 4 | Integer32 |  |
| -Julian_Day_1 | JulDay_1 | Integer | 4 | Integer32 |  |
| -Time_1 | Time_1 | Integer | 4 | Integer32 |  |
| -Lat._2, Long._2 | Lat_2, Long_2 | Float | 2 x4 | Float32 |  |
| -Altitude_2 | Alt_2 | Integer | 4 | Integer32 |  |
| -Julian_Day_2 | JulDay_2 | Integer | 4 | Integer32 |  |
| -Time_2 | Time_2 | Integer | 4 | Integer32 |  |
| *X1,Y1,Z1 | X1, Y1, Z1 | Float | 3 x 4 | Float32 |  |
| *X2,Y2,Z2 | X2, Y2, Z2 | Float | 3 x 4 | Float32 |  |
| -Sath_1, Sath_2 | Sath_1, Sath_2 | Float | 2 x 4 | Float32 |  |
| -Data_Rev_1 | DataRev_1 | integer | 4 | Integer32 |  |
| -Data_Rplus_1 | DataRplus_1 | integer | 4 | Integer32 |  |
| -QO_1 | QO_1 | integer | 4 | Integer32 | Quarter orbit designator for each scan: 1 (equator to NP) 2 (SP to equator) 3 (equator to SP) 4 (NP to equator) |
| Total size |  |  | 84 |  |  |

## Format of Z-Bits Ephemeris Record in Prep File.

There is one z-bit ephemeris record for all of the SSUSI sensor data records in a given scan.    Therefore, for imaging mode, there is 22 seconds in a scan so there will be one z-bit ephemeris record associated with all 22 seconds of the SSUSI sensor data.  For spectrograph mode, there is 3 seconds in a scan so there will be one z-bit ephemeris record associated with all 3 seconds of the SSUSI sensor data.   For test, maintenance and setup modes, there is 1 second in a scan so there will be one z-bit ephemeris record associated with each 1 second of the SSUSI sensor data.

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| -Ephemeris Clock Time - Part 1 | EphemClockPt1 | integer | 2 | 0..8,191 | Time in elapsed seconds since 0000Z of day of year (scaled integer when combined with part 2) |
| -Subpoint Longitude | SubpointLong | integer | 2 | 0..32,767 | Longitude of subsatellite point, WGS-72. (scaled integer) |
| -Word pair ID 1 | WordPairID1 |  | 1 | 1 | ID field for 32-bit word pair. |
| -Subpoint Latitude | SubpointLat | integer | 2 | 0..16,383 | Geodetic latitude of subsatellite point, WGS-72. (scaled integer) |
| -Cosine of Crossing Angle | CosCrossingAngle | integer | 2 | 0..8,191 | Cosine of crossing angle of subsatellite track with respect to local meridian (scaled integer) |
| -Word pair ID 2 | WordPairID2 |  | 1 | 2 | ID field for 32-bit word pair. |
| -Cosine of Solar Azimuth | CosSolarAzimuth | integer | 2 | 0..8191 | Azimuth of sun relative to direction of satellite flight (scaled integer) |
| -Solar Elevation | SolarElevation | integer | 2 | 0..16,383 | Elevation of sun with respect to local orbit tangent plane (scaled integer) |
| -Word pair ID 3 | WordPairID3 |  | 1 | 3 | ID field for 32-bit word pair. |
| -Height to earth radius ratio | HeightEarthRadiusRatio | integer | 2 | 0..8,191 | Altitude of spacecraft above subsatellite point at mean sea level (scaled integer) |
| -Ephemeris Clock Time - Part 2 | EphemClockPt2 | integer | 2 | 0..32,767 | Time in elapsed seconds since 0000Z of day of year (scaled integer when combined with part 1) |
| -Word pair ID 4 | WordPairID4 |  | 1 | 4 | ID field for 32-bit word pair. |
| -Cosine of Lunar Azimuth | CosLunarAzimuth | byte | 1 | 0..127 | Azimuth of moon relative to direction of satellite flight |
| -Lunar Elevation | LunarElevation | integer | 2 | 0..4095 | Elevation of moon with respect to local orbit tangent plane |
| -Lunar Phase | LunarPhaseAngle | byte | 1 | 0..255 | Angle between lunar and solar pos. vectors in ECI frame |
| -Word pair ID 5 | WordPairID5 |  | 1 | 5 | ID field for 32-bit word pair |
| Total size |  |  | 25 |  |  |

## SSUSI Sensor Data Record.

The data in this record comprises all of the SSUSI sensor packets (up to 22) within a given SSUSI instrument scan.  The number of packets is determined by the instrument mode(s) within a given instrument scan period.  Note that the instrument can change modes in the middle of a scan although it generally needs to go into setup mode prior to switching to the final mode.

Therefore, for imaging mode, there is 22 seconds in a scan so there will be one ephemeris record associated with all 22 seconds of the SSUSI sensor data, provided you are in imaging mode for the entire 22 seconds.  For spectrograph mode, there is 3 seconds in a scan so there will be one ephemeris record associated with all 3 seconds of the SSUSI sensor data, provided you are in spectrograph mode for the entire 3 seconds.   For test, maintenance and setup modes, there is 1 second in a scan so there will be one ephemeris record associated with each 1 second of the SSUSI sensor data.

Note:  An existing SSUSI Sensor Data Record will be completed for the following reasons:

- The SSUSI instrument was in the same mode for the entire duration of the scan.  This is a normal termination.

- The SSUSI instrument changed modes within a scan.  In this case, a SSUSI sensor data record will be output for the original mode, containing all of the sensor data packets that occurred while in the original mode.  Then, an additional SSUSI sensor data record will be output for the new mode containing all of the sensor data packets for that instrument mode.

## Sensor Data Packet Record.

Consists of one second of SSUSI sensor data, or rather one SSUSI sensor packet.  There are 51 different types of SSUSI sensor packets numbered 0 through 50.  Each Sensor Data Packet Record consists of a single SSUSI Sensor Data Packet Header and a single SSUSI Sensor Packet.

## Sensor Data Packet Header

This appears once per sensor data packet record which occurs for every single packet of SSUSI sensor data at a frequency of once every second.

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| -OLS sync code | OLSSyncCode | byte | 5 | 23378884798 only | OLS message sync code |
| -OLS time | OLSTime | integer | 4 | 0..100,000,000 | Natural32 |
| -Packet count | PacketCount | byte | 1 | 0..63 | Sequence of packet in readout |
| -Packet ID | PacketID | byte | 1 | 1 .. 150 | Flags Fill Packet when ID = 0 or when 51 < ID < 100 |
| Imaging scan mode | Scan_Mode | Char | 1 | “Full” or “Reduced” | This field occurs only in imaging mode data. |
| Lat_1sec | Lat_1sec | Int | 4 | -9000…9000 |  |
| Long_1sec | Long_1sec | Int | 4 | 0000..360000 |  |
| Alt_1sec | Alt_1sec | Int | 4 | 40000..50000 |  |
| Total size |  |  | 23 |  |  |

## Packet Data formats by Packet ID

### Fill Packets

Format of Fill Packet Record in Prep File;  Packet ID = 0

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| data bits | DataBits | byte | 475 | 0 | All 3796 data bits set to 0 for fill packet. |
| Total size |  |  | 486 |  |  |

### Full Image Scan

#### Format of First Scan Image Mode Record in Prep File;  Packet ID = 1 through 21

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photometer427Count | Array of long (expand to a long) | 4 * 22 with 22nd index from Last Scan Image Mode, Packet ID 22 | 0..4,194,303 |  |
| Photometer 629, 630 count | Photometer629Count Photometer630Count | Array of long (expand to a long) | 2 x 4 * 22 with 22nd index from Last Scan Image Mode, Packet ID 22 | 0..2,097,151 |  |
| Image Pixel Data | PixelData1 | Array of byte | 622 * 21 | 0..63 | 622 Full scan pixels |
| Total size |  |  | 645 |  |  |

#### Format of Last Scan Image Mode Record in Prep File;  Packet ID = 22

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photometer427Count | Array of Integer (expand to a long) | 4 * 22 with 1st .. 21st index from First Scan Image Mode, Packet ID 1-21 | 0..4,194,303 |  |
| Photometer 629, 630 count | Photometer629_630Count | Array of Integer (expand to a long) | 2 x 4 * 22 with 1st .. 21st index from First Scan Image Mode, Packet ID 1-21 | 0..2,097,151 |  |
| Image Pixel Data | PixelData2 | byte | 378 | 0..63 | Full scan pixels |
| Detector Processing Ratio | DetectorRatio | byte | 180 | 0..63 | Full scan pixels |
| Pulse Height Data | PulseHeightData | Integer | 3 x 2 |  |  |
| Flight Software Version Number | Flight_SW_Version | byte | 1 |  |  |
| SSUSI Color Table Version Number | Flight_SW_ColorTable_Version | byte | 1 |  |  |
| 427, 629, 630 Filter Heater On | Filter427Heater Filter629Heater Filter630Heater | byte | 3 x 1 |  |  |
| Dark, Background Count | DarkCount BackgroundCount | integer | 2 x 2 | 0..65,535 |  |
| Start position | MirrorStartPosition | integer | 2 | 0..4,095 |  |
| Nadir Position | NadirPosition | integer | 2 | 0..4,095 |  |
| Fault Status | FaultStatus | byte | 1 | 0, 1 | Fault status booleans |
| Previous Commands 1, 2 | PrevCommand1 PrevCommand2 | byte | 2 * 1 | 0 .. 255 | Last command from OLS |
| FIFO Status | FIFOStatus | byte | 1 | 0, 1 | FIFO status booleans |
| OLS reference count | OLSRefCount | byte | 1 | 0..255 |  |
| SIS status | SISStatus | Integer | 2 | 0,1 | SSUSI status register booleans |
| Photometer status | PhotometerStatus | byte | 1 | 0,1 | Command mode, photom., SIS selection booleans |
| Detector configuration | DetectorConfig | byte | 1 | 0,1 | Booleans for control input to SIS FPE units. |
| Detector HVPS set | DetectorHighVoltage | byte | 1 | 0..255 |  |
| 427, 629, 630 Filter Set Temp | Filter427SetTemp Filter629SetTemp Filter630SetTemp | byte | 3 x 1 | 0..255 |  |
| 427, 629, 630 Filter Temp | Filter427Temp Filter629Temp Filter630Temp | byte | 3 x 1 | 0..255 |  |
| PHVPS temp | PHVPSTemp | byte | 1 | 0..255 |  |
| Primary, Backup illum. sensor | IllumSensor1 IllumSensor2 | byte | 2 x 1 | 0..255 |  |
| 427, 629, 630 Phot. HV | Photometer427HighVoltage Photometer629HighVoltage Photometer630HighVoltage | byte | 3 x 1 | 0..255 |  |
| SIS radiator , Scan mirror temp | SISRadiatorTemp ScanMirrorTemp | byte | 2 x 1 | 0..255 |  |
| Primary , Secondary detector HV | Det1HighVoltage Det2HighVoltage | byte | 2 x 1 | 0..255 |  |
| Primary , Secondary FPE temp | FPE1Temp FPE2Temp | byte | 2 x 1 | 0..255 |  |
| SM I/O board temp | SMBoardTemp | byte | 1 | 0..255 |  |
| Scan motor current | ScanMotorCurrent | byte | 1 | 0..255 |  |
| Total size |  |  |  |  |  |

So, if in Full Scan Imaging mode for the entire 22 seconds, the SSUSI Sensor Data Packet Record will be depicted as:

### Reduced Scan Packets

#### Format of First Reduced Scan Mode Record in Prep File;  Packet ID = 23 through 43

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| -Photometer 427 count | Photometer427Count | Array of long | 4 * 22 with 22nd index from Last Scan Image Mode, Packet ID 44 | 0..4,194,303 |  |
| -Photometer 629, 630 counts | Photometer629Count Photometer630Count | Array of long | 2 x 4 * 22 with 22nd index from Last Scan Image Mode, Packet ID 44 | 0..2,097,151 |  |
| -Image Pixel Data (533 counts) | PixelData1 | Array of byte | 533 * 21 | 0..127 | Reduced-scan pixels |
| Total size |  |  |  |  |  |

#### Format of Last Reduced Scan Mode Record in Prep File;  Packet ID = 44

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| -Photometer 427 count | Photometer427Count | Array of long | 4 * 22 with 1st - 21nd index from first Scan Image Mode, Packet ID 23 - 43 | 0..4,194,303 |  |
| -Photometer 629, 630 counts | Photometer629Count Photometer630Count | Array of long | 2 x 4 * 22 with 1st - 21nd index from first Scan Image Mode, Packet ID 23 - 43 | 0..2,097,151 |  |
| -Image Pixel Data | PixelData2 | byte | 327 | 0..127 | Reduced scan pixels |
| -Detector processing ratios | DetectorRatio | byte | 156 | 0..63 | 156 across-track scan steps |
| -Pulse Height data | PulseHeightData | integer | 2 x 15 | 0..1023 | Wedge, strip,. intermediate, other pulse height |
| -Flight Software Version Number | Flight_SW_Version | byte | 1 |  |  |
| -SSUSI Color Table Version Number | Flight_SW_ColorTable_Version | byte | 1 |  |  |
| -427,629,630 Filter Heater On | Filter427Heater Filter629Heater Filter630Heater | byte | 3 x 1 |  |  |
| -Dark, Background Count | DarkCount BackgroundCount | integer | 2 x 2 | 0..65,535 |  |
| -Start position, nadir position | MirrorStartPosition NadirPosition | integer | 2 x 2 | 0..4,095 |  |
| -Fault Status | FaultStatus | byte | 1 | 0, 1 | Fault status booleans |
| -Previous Commands 1, 2 | PrevCommand1 PrevCommand2 | byte | 2 * 1 | 0..255 | Last command from OLS |
| -FIFO Status | FIFOStatus | byte | 1 | 0, 1 | FIFO status booleans |
| -OLS reference count | OLSRefCount | byte | 1 | 0..255 |  |
| -SIS status | SISStatus | integer | 2 | 0,1 | SSUSI status register booleans |
| -Photometer status | PhotometerStatus | byte | 1 | 0,1 | Command mode, photom., SIS selection booleans |
| -Detector configuration | DetectorConfig | byte | 1 | 0,1 | Booleans for control input to SIS FPE units. |
| -Detector HVPS set | DetectorHighVoltage | byte | 1 | 0..255 |  |
| -427,629,630 filter Set Temp | Filter427SetTemp Filter629SetTemp Filter630SetTemp | byte | 1 x 3 | 0..255 |  |
| -427,629,630 filter Temp | Filter427Temp Filter629Temp Filter630Temp | byte | 1 x 3 | 0..255 |  |
| -PHVPS temp | PHVPSTemp | byte | 1 | 0..255 |  |
| -Primary, Backup illumination sensor | IllumSensor1 IllumSensor2 | byte | 1 x 2 | 0..255 |  |
| -Photom. 427, 629, 630 HV | Photometer427HighVoltage Photometer629HighVoltage Photometer630HighVoltage | byte | 1 x 3 | 0..255 |  |
| -SIS radiator, scan mirror temp | SISRadiatorTemp ScanMirrorTemp | byte | 1 x 2 | 0..255 |  |
| -Primary, secondary detector HV | Det1HighVoltage Det2HighVoltage | byte | 1 x 2 | 0..255 |  |
| -Primary, secondary FPE temp | FPE1Temp FPE2Temp | byte | 1 x 2 | 0..255 |  |
| -SM I/O board temp | SMBoardTemp | byte | 1 | 0..255 |  |
| -Scan motor current | ScanMotorCurrent | byte | 1 | 0..255 |  |
| Total size |  |  |  |  |  |

So, if in Reduced Scan Imaging mode for the entire 22 seconds, the SSUSI Sensor Data Packet Record will be depicted as:

### Spectrograph mode

#### Format of First Spectrograph Mode Record in Prep File;  Packet ID = 45 or 46

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photomter427Count | long | 4 | 0..4,194,303 |  |
| Photometer 629, 630 counts | Photometer629Count Photometer630Count | long | 2 x 4 | 0..2,097,151 |  |
| Spectrograph Data | PixelData1 | byte | 466 | 0..255 | 466 Spectrograph counts |
| Total size |  |  |  |  |  |

#### Format of Last Spectrograph Mode Record in Prep File;  Packet ID = 47

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photomter427Count | long | 4 | 0..4,194,303 |  |
| Photometer 629, 630 counts | Photometer629Count Photometer630Count | long | 2 x 4 | 0..2,097,151 |  |
| Spectrograph Data | PixelData2 | byte | 412 | 0..255 | 412 Spectrograph counts |
| Flight Software Version Number | Flight_SW_Version | byte | 1 |  |  |
| Pulse height data | PulseHeightData | integer | 3 x 2? | 0..1023 | Wedge, strip,. intermediate, other pulse height |
| Scan Mirror Position | MirrorPosition | integer | 2 | 0..4095 |  |
| Detector input, output rate | DetInputRate DetOutputRate | long | 2 x 4 | 0..4,294,967,295 |  |
| Dark Count | DarkCount | integer | 2 | 0..65535 |  |
| Fault Status | FaultStatus | byte | 1 | 0,1 | fault status booleans |
| Previous Commands 1, 2 | PrevCommand1 PrevCommand2 | byte | 2 x 1 | 0..255 | last command from OLS |
| FIFO Status | FIFOStatus | byte | 1 | 0,1 | FIFO status booleans |
| OLS reference count | OLSRefCount | byte | 1 | 0..255 |  |
| SIS status | SISStatus | byte | 2 | 0,1 | SSUSI status register booleans |
| Photometer status | PhotometerStatus | byte | 1 | 0,1 | Command mode, photom., SIS selection booleans |
| Detector configuration | DetectorConfig | byte | 1 | 0,1 | Booleans for control input to SIS FPE units. |
| Detector HVPS set | DetectorHighVoltage | byte | 1 | 0..255 |  |
| 427,629,630 filter Set Temp | Filter427SetTemp Filter629SetTemp Filter630SetTemp | byte | 3 x 1 | 0..255 |  |
| 427,629,630 filter Temp | Filter427Temp Filter629Temp Filter630Temp | byte | 3 x 1 | 0..255 |  |
| PHVPS temp | PHVPSTemp | byte | 1 | 0..255 |  |
| Primary, Backup illumination sensor | IllumSensor1 IllumSensor2 | byte | 2 x 1 | 0..255 |  |
| Photometer 427, 629, 630 HV | Photometer427HighVoltage Photometer629HighVoltage Photometer630HighVoltage | byte | 3 x 1 | 0..255 |  |
| SIS radiator, scan mirror temp | SISRadiatorTemp ScanMirrorTemp | byte | 2 x 1 | 0..255 |  |
| Primary, secondary detector HV | Det1HighVoltage Det2HighVoltage | byte | 2 x 1 | 0..255 |  |
| Primary, secondary FPE temp | FPE1Temp FPE2Temp | byte | 2 x 1 | 0..255 |  |
| SM I/O board temp | SMBoardTemp | byte | 1 | 0..255 |  |
| Scan motor current | ScanMotorCurrent | byte | 1 | 0..255 |  |
| Total size |  |  |  |  |  |

So, if in Spectrograph mode for the entire 3 seconds, the SSUSI Sensor Data Packet Record will be depicted as:

### Maintenance Mode

Format of Maintenance Mode Records in Prep File;  Packet ID = 48

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photometer427Count | long | 4 | 0..4,194,303 |  |
| Photometer 629, 630 counts | Photometer629Count Photometer630Count | long | 2 x 4 | 0..2,097,151 |  |
| Source, Dest, Count, & Increment Registers | SourceRegister DestRegister CountRegister IncrementRegister | integer | 4 x 2 | 0..65,535 |  |
| Memory Page | MemoryPage | byte | 1 | 0..255 |  |
| Memory Address | MemoryAddress | Integer | 2 | 0..65,535 |  |
| Memory Data Dump | MemoryDataDump | byte | 423 | 0..255 | dump 423, |
| Upload Checksum | UploadChecksum | integer | 2 |  |  |
| Fault Status | FaultStatus | byte | 1 | 0,1 | fault status booleans |
| Previous Commands 1, 2 | PrevCommand1 PrevCommand2 | byte | 2 x 1 | 0..255 | last command from OLS |
| FIFO Status | FIFOStatus | byte | 1 | 0,1 | FIFO status booleans |
| OLS reference count | OLSRefCount | byte | 1 | 0..255 |  |
| SIS status | SISStatus | integer | 2 | 0,1 | SSUSI status register booleans |
| Photometer status | PhotometerStatus | byte | 1 | 0,1 | Command mode, photom., SIS selection booleans |
| Detector configuration | DetConfig | byte | 1 | 0,1 | Booleans for control input to SIS FPE units. |
| Detector HVPS set | DetHighVoltage | byte | 1 | 0..255 |  |
| 427,629,630 filter Set Temp | Filter427SetTemp Filter629SetTemp Filter630SetTemp | byte | 3 x 1 | 0..255 |  |
| 427,629,630 filter Temp | Filter427Temp Filter629Temp Filter630Temp | byte | 3 x 1 | 0..255 |  |
| PHVPS temp | PHVPSTemp | byte | 1 | 0..255 |  |
| Primary, Backup illumination sensor | IllumSensor1 IllumSensor2 | byte | 2 x 1 | 0..255 |  |
| Photometer 427, 629, 630 HV | Photometer427HighVoltage Photometer629HighVoltage Photometer630HighVoltage | byte | 3 x 1 | 0..255 |  |
| SIS radiator, scan mirror temp | SISRadiatorTemp ScanMirrorTemp | byte | 2 x 1 | 0..255 |  |
| Primary, secondary detector HV | Det1HighVoltage Det2HighVoltage | byte | 2 x 1 | 0..255 |  |
| Primary, secondary FPE temp | FPE1Temp FPE2Temp | byte | 2 x 1 | 0..255 |  |
| SM I/O board temp | SMBoardTemp | byte | 1 | 0..255 |  |
| Scan motor current | ScanMotorCurrent | byte | 1 | 0..255 |  |
| Total size |  |  |  |  |  |

So, in Maintenance mode, the SSUSI Sensor Data Packet Record will be depicted as:

### Setup Mode

Format of Setup Mode Records in Prep File;  Packet ID = 49

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photometer427Count | long | 4 | 0..4,194,303 |  |
| Photometer 629, 630 counts | Photmoter629Count Photometer630Count | long | 2 x 4 | 0..2,097,151 |  |
| Source, Dest, Count, & Increment Registers | SouceRegister DestRegister CountRegister IncrementRegister | integer | 4 x 2 | 0..65,535 |  |
| Memory Page | MemoryPage | byte | 1 | 0..255 |  |
| Memory Address | MemoryAddress | integer | 2 | 0..65,535 |  |
| Memory Data Dump | MemoryDataDump | byte | 418 | 0..255 | Dump 418 |
| Flight Software Version Number | Flight_SW_Version | byte | 1 |  |  |
| Scan Mirror Position | MirrorPositoin | integer | 2 |  |  |
| Detector Input Rate | DetInputRate | integer | 4 | 0..4,294,967,295 |  |
| Fault Status | FaultStatus | byte | 1 | 0,1 | fault status booleans |
| Previous Commands 1, 2 | PrevCommand1 PrevCommand2 | byte | 2 x 1 | 0..255 | last command from OLS |
| FIFO Status | FIFOStatus | byte | 1 | 0,1 | FIFO status booleans |
| OLS reference count | OLSRefCount | byte | 1 | 0..255 |  |
| SIS status | SISStatus | integer | 2 | 0,1 | SSUSI status register booleans |
| Photometer status | PhotometerStatus | byte | 1 | 0,1 | Command mode, photom., SIS selection booleans |
| Detector configuration | DetConfig | byte | 1 | 0,1 | Booleans for control input to SIS FPE units. |
| Detector HVPS set | DetHVPS | byte | 1 | 0..255 |  |
| 427,629,630 filter Set Temp | Filter427SetTemp Filter629SetTemp Filter630SetTemp | byte | 3 x 1 | 0..255 |  |
| 427,629,630 filter Temp | Filter427Temp Filter629Temp Filter630Temp | byte | 3 x 1 | 0..255 |  |
| PHVPS temp | PHVPSTemp | byte | 1 | 0..255 |  |
| Primary, Backup illumination sensor | IllumSensor1 IllumSensor2 | byte | 2 x 1 | 0..255 |  |
| Photometer 427, 629, 630 HV | Photometer427HighVoltage Photometer629HighVoltage Photometer630HighVoltage | byte | 3 x 1 | 0..255 |  |
| SIS radiator, scan mirror temp | SISRadiatorTemp ScanMirrorTemp | byte | 2 x 1 | 0..255 |  |
| Primary, secondary detector HV | Det1HighVoltage Det2HighVoltage | byte | 2 x 1 | 0..255 |  |
| Primary, secondary FPE temp | FPE1Temp FPE2Temp | byte | 2 x 1 | 0..255 |  |
| SM I/O board temp | SMBoardTemp | byte | 1 | 0..255 |  |
| Scan motor current | ScanMotorCurrent | byte | 1 | 0..255 |  |
| Total size |  |  |  |  |  |

So, in Setup mode, the SSUSI Sensor Data Packet Record will be depicted as:

### Test Mode

Format of Test Mode Records in Prep File; Packet ID = 50

| Field | NetCDF Variable Name | Data Type | Bytes | Range | Content |
| --- | --- | --- | --- | --- | --- |
| Sensor data packet header |  | N/A | 11 | N/A |  |
| Photometer 427 count | Photometer427Count | long | 4 | 0..4,194,303 |  |
| Photometer 629, 630 counts | Photometer629Count Photometer630Count | long | 2 x 4 | 0..2,097,151 |  |
| Flight Software Version Number | Flight_SW_Version | byte | 1 | 0..15 | An abbreviated flight s/w version number since there is only room for 4 bits in the sensor telemetry data. All other instrument modes have 8 bits in the sensor telemetry data. |
| DPU Test results | DPUTestResult | byte | 16 | 0..255 |  |
| Pulse Height data | PulseHeightData | long | 333 x 2 | 0.. 4,194,303 |  |
| Detector input rate | DetInputRate | integer | 4 | 0..65,535 |  |
| Fault Status | FaultStatus | byte | 1 | 0,1 | fault status booleans |
| Previous Commands 1, 2 | PrevCommand1 PrevCommand2 | byte | 2 x 1 | 0..255 | last command from OLS |
| FIFO Status | FIFOStatus | byte | 1 | 0,1 | FIFO status booleans |
| OLS reference count | OLSRefCount | byte | 1 | 0..255 |  |
| SIS status | SISStatus | integer | 2 | 0,1 | SSUSI status register booleans |
| Photometer status | PhotometerStatus | byte | 1 | 0,1 | Command mode, photom., SIS selection booleans |
| Detector configuration | DetConfig | byte | 1 | 0,1 | Booleans for control input to SIS FPE units. |
| Detector HVPS set | DetHVPSSet | byte | 1 | 0..255 |  |
| 427,629,630 filter Set Temp | Filter427SetTemp Filter629SetTemp Filter630SetTemp | byte | 3 x 1 | 0..255 |  |
| 427,629,630 filter Temp | Filter427Temp Filter629Temp Filter630Temp | byte | 3 x 1 | 0..255 |  |
| PHVPS temp | PHVPSTemp | byte | 1 | 0..255 |  |
| Primary, Backup illumination sensor | IllumSensor1 IllumSensor2 | byte | 2 x 1 | 0..255 |  |
| SIS radiator, scan mirror temp | SISRadiatorTemp ScanMirrorTemp | byte | 2 x 1 | 0..255 |  |
| Primary, secondary detector HV | Det1HighVoltage Det2HighVoltage | byte | 2 x 1 | 0..255 |  |
| Primary, secondary FPE temp | FPE1Temp FPE2Temp | byte | 2 x 1 | 0..255 |  |
| SM I/O board temp | SMBoardTemp | byte | 1 | 0..255 |  |
| Scan motor current | ScanMotorCurrent | byte | 1 | 0..255 |  |
| Total size |  |  |  |  |  |

So, when in Test Mode,  SSUSI Sensor Data Packet Record will be depicted as:

## Supporting Data Prep File.

This is an ancilliary file that will be implemented after launch and will be propagated as a function of time, in reverse chronological order with the ephemeris and z-bit records at a 1 second resolution.

| Data Item | Data Type | Field Size (Bytes) | Range or Nominal Value | Units |
| --- | --- | --- | --- | --- |
| Header | N/A | 1637 | N/A | N/A |
| GWC Ephemeris Record | N/A |  | N/A | N/A |
| Z-Bits Ephemeris Record | N/A |  | N/A | N/A |

Total Prep Data file:

Header:			1637 bytes

Data per scan:		57 bytes *  (min. orbit / sec. Scan) = bytes

Imaging data per scan:	81,748 bytes * (min. orbit / sec. Scan) = bytes

Total:			bytes = ~ Mbytes per orbit