## Slide 1: DATA Usage Information
Robert Schaefer for The SSUSI Team

## Slide 2: Analyzing SSUSI data – What variables to use?
Many Variables to Choose From, Many Quality Indicators – What do I use?
  Need coordinates
  Variables of interest
  Other environmental parameters
Some files contain many variables (particularly L1B) that are not needed for basic analysis
This guide is intended to show only the most commonly used variables to help users get started with data – there is much more information in these files to be explored!

## Slide 3: Time
Files all have a header (called global attributes in NetCDF)
  Headers for all SSUSI files have data start and data end times so time range can be quickly identified: fileds are strings - eg, 2004150100727 (day 150 or 2004 at 10:07:27 UT)
All files contain variables with
  YEAR (North or South_time_Pred_Year in EDR-AURORA-PRED)
  DOY for Day Of Year (North or South_time_Pred_Doy in EDR-AURORA-PRED)
  Seconds of the day
    TIME in L1B, SDR, and all EDRs except EDR-AURORAL and EDR-AURORA-PRED
    EDR-AURORAL: UT_N and UT_S for Northern and Southern hemispheres, respectively – these are the seconds of the day that correspond to each bin of the Mlat, MLT grid
    EDR-AURORA-PRED: North_TIME_UT_pred, South_time_UT_pred

## Slide 4: Coordinates for Geolocation
On the limb, coordinates are relatively easy - use tangentpoint geolocation – the point directly below where look vector comes closest to the Earth’s surface
On disk, we know the UV is not coming from the Surface (troposphere opaque to UV)
Where to geolocate?
Choose typical emission altitudes and piercepoint shells
Piercepoint – imagine a shell of constant height above the surface – the “piercepoint” is where the look vector pierces that shell.
Piercepoint shell altitudes:
  Auroral – 110 km
  Day – 150 km
  Night – 350 km
SSUSI Products give geolocations for all 3 altitudes globally to allow maximum flexibility for analysis
As a user – your task is to determine which set of coordinates to use and where the boundaries of your analysis are

## Slide 5: Pixel Geolocations depend on altitude
SSUSI
Look vector
Night Shell
350 km
Day Shell
150 km
SSUSI Products determine geolocations for all 3 altitudes globally to allow maximum flexibility
Geolocation is different for different altitudes

## Slide 6: There is voluminous documentation in Algorithm Description documents
Detailed prescription for geolocation of pixels is given in the document. (Section 3.5)
Describes how data is gridded – with details about the sizes of the pixels.
Describes how each parameter is retrieved.
The main document describes all of our most recent work on the algorithms.
There is also a large “Appendix” that describes the original algorithms defined in the 1990s, some of which are still in use:
  Nightside Disk - NmF2, HmF2
  Dayside Limb – O, O2, N2, TEC, NmF2, HmF2
  The validity of these algorithms is questionable and they should be updated.
  We are working to replace the functionality in the Nightside Disk algorithm with the 3D ionosphere product.

## Slide 7: Variables – Radiances and Gridding
For those who want to do everything themselves – use the Level1B files – you will need help with these, but you’re in it for the long haul.
For those who want to use gridded radiances -Choose grid size and geolocation altitude
  SDR-DISK – high resolution (e.g. 25 x 50 km2) mainly used for visualization
  SDR2-DISK – lower resolution (e.g. 100 x 200 km2) mainly used for EDR retrievals
  Note SDR2-DISK also has a very coarse resolution grid (e.g. 300 x 600 km2) for global model data assimilation – variables for this contain the string GAIM as it was designed for the Utah State U GAIM model.

## Slide 8: Radiances (L1B)
Color_index: 0=1216, 1=1304, 2=1356, 3=LBHS, 4=LBHL
L1B arrays
  DISK: LIMB_RADIANCEDATA_INTENSITY[color, cross_track, along_track, scan_number]
  LIMB: LIMB_RADIANCEDATA_INTENSITY[color, altitude_index, along_track, scan_number]
  Errors
    Photon counting errors: DISK_COUNTERROR_TOTAL, LIMB_COUNTERROR_TOTAL
    Systematic errors in calibration: DISK_CALIBRATIONERROR, LIMB_CALIBRATIONERROR
Data Quality Indices (mainly used if MeV noise is present. Radiances are corrected for MeV noise only in the SAA)
  DQI_TOTAL_SCAN: If there are problems with the whole scan these are set. Use data if DQI_TOTAL=0
  DQI_TOTAL_COLOR: if there is a problem with the treatment of a specific color, then this is set, use if DQI_TOTAL_COLOR=0
Also useful are photon counts – background subtraction is done in count space. All removed background (counts) are stored in the L1B, but these are mainly for more expert users

## Slide 9: Radiances (SDR)
DISK (SDR-DISK & SDR2-DISK)
  DISK_INTENSITY_*
  DISK_RADIANCE_UNCERTAINTY_*
  Where * = DAY, NIGHT, AURORAL
  Pixels in SDR-DISK (25 x 50 km2), in SDR2-DISK (100 x 200 km2)
LIMB (SDR-LIMB)
  LIMB_INTENSITY
  LIMB_RADIANCE_UNCERTAINTY
  Altitude steps of ~20 km, alongtrack size = 100 km.
Similar variables with “GAIM” in the name – much coarser resolution
Data Quality Indices
  Disk: DQI_NIGHT, DQI_DAY, DQI_DAY_AURORAL
  Limb: DQI
  Values are bit 0=MeV noise, 1=SAA, and 2=F18 instrument problem
  Note radiances have been corrected for particle noise in the SAA so you can use data where (DQI and 3) = 3, since MeV noise flag will also be set in the SAA. MeV noise is also set in the auroral zone when particle noise is detected

## Slide 10: Radiances – Auroral Region in EDR-AURORAL
Auroral binned in magnetic coordinates (Mlat, MLT)
Radiances in EDR-AURORA have Dayglow and MeV particle noise removed and are therefore can be different than what is in the SDR (or L1B).
  DISK_RADIANCEDATA_INTENSITY_NORTH[color_index, geomagnetic_longitude_index, geomagnetic_latitude_index]
  DISK_RADIANCEDATA_INTENSITY_SOUTH[color_index, geomagnetic_longitude_index, geomagnetic_latitude_index]
Quality Indices
  DATA_QUALITY_GLOBAL – whether there might be a problem with the basic file inputs – use data if this is 0 (only set if unexpected pointing problem arises with F18)
  DATA_QUALITY – Best data is when DATA_QUALITY = 0. Weak aurora flagged in bits 2 and 3. If aurora is in dayside or MeV noise has been removed, bit 1or bit 0 is set to 1 – aurora will be noisier due to large background removed.
    Bit # Meaning if set to true
    0 MeV noise
    1 Dayside
    2 Fair; 0.2<=Q<=2 & nightside & no MeV noise
    3 Poor; Q < 0.2 ergs/s/cm**2, or dayside, or MeV noise

## Slide 11: Auroral Environmental Parameters
Variables use geomagnetic coordinates:
  LATITUDE_GEOMAGNETIC_GRID_MAP, MLT_GRID_MAP
  Note: There is only one set of these for north and south – but for south, you must multiply the magnetic latitude by -1.
Energy Flux – Mean Energy
  ENERGY_FLUX_NORTH_MAP, ENERGY_FLUX_SOUTH_MAP [geomagnetic_longitude_index,geomagnetic_latitude_index]
  ELECTRON_MEAN_NORTH_ENERGY_MAP, ELECTRON_MEAN_SOUTH_ENERGY_MAP[geomagnetic_longitude_index,geomagnetic_latitude_index]
Electron Densities
  HmE (HME_NORTH, HME_SOUTH)
  NmE (NME_NORTH, NME_SOUTH)
Hemispheric Power
  HEMISPHERE_POWER_NORTH, HEMISPHERE_POWER_SOUTH
MANY OTHER VARIABLES FOR MORE EXPERT USE

## Slide 12: EDR-IONO 3D electron densities
Coordinates for 3D electron densities (ED_ALT, and then either ED_LAT, ED_LON, or ED_MLAT, ED_MLON)
Electron Densities
  ED_CUBE
  ED_ERROR
Data quality
  Global data quality in Global attributes DATA_QUALITY_INDEX, use if =0. (only flagging if potential F18 pointing problem exists, or if MeV noise has been subtracted

## Slide 13: EDR-IONO Bubble Characteristics
NDEPS - If no Ionospheric Bubbles have been detected, NDEPS=0 and the file does not need to be considered further. If nonzero NDEPS is the number of bubbles detected
Coordinates of Bubble Centroid: CENTROID_LAT, CENTROID_LON, CENTROID_ALT [NDEPS]
Volume of bubble in km3: DVOL[NDEPS]
Electron density in bubble:
  MEDIAN_DEP[NDEPS]
  MEDIAN_DEP_ERROR[NDEPS]